## Slide 1: Checking SOAPY simulation
PhD meeting
Puttiwat Kongkaew
05 June 2023

## Slide 2: Includes
Review of 22/05/23 meeting
This week research
Plan

## Slide 3: Review of 22/05/2023 meeting
Meeting online with Tim
No progress on new thesis chapter
Skip analysis on phase screen and propagation.
Generation of interaction and control matrix looks nice. Must check performance dependence on svd.
Reconstructor converges to theoretical performance (DM fitting error)
Delay error looks promising. Must reduce error bar.

## Slide 4: Review of 22/05/2023 meeting
Plan for 23/05 – 05/06/2023
  Check reconstructor performance as svd changes.
  Reduce error bar on delay analysis.
  Turbulence Temporal PSD
  Slope covariance
  Study SLODAR

## Slide 5: Effect of SVD on reconstructor performance




?





Before the drop
After the drop
between
Suitable value  any between the drop points (0.130 – 0.019)

## Slide 6
Strehl ratio
Time (s)

## Slide 7: Temporal error
Frame rate = 0.0025s
R0 = 5cm
Max error = 1.029(d/r)^(5/3)
L0 = 8m
Lenslet Diameter = 0.4m/8 = 5cm
l0 = 1e-10 m (hard code in soapy)
Plateau region is
the lower of either
Limited to r0/frame
or
Noll’s telescope size
Frame rate = 0.0025s
R0 = 2.5cm – 75m
Max error = 1.029(d/r)^(5/3)
L0 = 8m
Lenslet Diameter = 0.4m/8 = 5cm
l0 = 1e-10 m (hard code in soapy)
Coherence time instead of r0?

## Slide 8: Turbulence Temporal PSD
Starting to see noisy region?
AO correction
Performance gain by AO
AO-amplified error
Frame = 0.001s
Total time = 1s
R0 = 5cm
L0 = 10m
Tel = 0.4m
Nxsub = 8
Pxlspersubap = 16
dm gain = 1
Vbar5/3=15.11m/s
Vmin = 5m/s
Vmax=34.53
Tau0=1.04ms
Fmax=1/2pixeltime
pixel time = 0.4m/16/8/5m/s
= 0.625ms
max frequency = 1/(2*pxtime)
= 1/(2*0.625ms) = 800Hz
Correct units??

## Slide 9
Tip/tilt frequency (Hz)
Power spectral density
Greenwood frequency
Corrected
Uncorrected

## Slide 10: Turbulence Temporal PSD
What happen here?
Frame = 0.0001s
Total time = 0.25s
R0 = 5cm
L0 = 10m
Tel = 0.4m
Nxsub = 8
Pxlspersubap = 16
dm gain = 1
Vbar5/3=15.11m/s
Vmin = 5m/s
Vmax=34.53
Tau0=1.04ms
Usual FT limit
Calculation limit
Can be fix by
Frame rate
Pixel shift limit
Atm Layers
= Not what happen
Physically
Can be fix by
reducing pixel scale
L0 frequency
Nyquist frequencies of each layer
Correct units??

## Slide 11: Turbulence Temporal PSD
Frame = 0.0001s
Total time = 0.25s
R0 = 5cm
L0 = 10m
Tel = 0.4m
Nxsub = 8
Pxlspersubap = 16
dm gain = 1
Vbar5/3=15.11m/s
Vmin = 5m/s
Vmax=34.53
Tau0=1.04ms
Usual FT limit
Calculation limit
Can be fix by
Frame rate
subap shift limit
Atm Layers
= is what ao see
So this is legit still.
L0 frequency
subap frequencies of each layer
Correct units??

## Slide 12: Turbulence Temporal PSD
Usual FT limit
Calculation limit
Can be fix by
Increase frame rate
subap shift limit
= is what ao see
So this is legit still.
Frame = 0.0001s
Total time = 0.25s
R0 = 5cm
L0 = 10m
Tel = 0.4m
Nxsub = 8
Pxlspersubap = 16
dm gain = 1
Vbar5/3=15.11m/s
Vmin = 5m/s
Vmax=34.53
Tau0=1.04ms
Pixel shift limit
- Not what happen physically
- Can be fix by
reducing pixel scale
Correct units??
error

## Slide 13: Turbulence Temporal PSD
Usual FT limit
Calculation limit
Can be fix by
Increase frame rate
subap shift limit
= is what ao see
So this is legit still.
Frame = 0.000625s
Total time = 1s
R0 = 5cm
L0 = 10m
Tel = 0.4m
Nxsub = 8
Pxlspersubap = 16
dm gain = 1
Vbar5/3=15.11m/s
Vmin = 5m/s
Vmax=34.53
Tau0=1.04ms
Pixel shift limit
- Not what happen physically
- Can be fix by
reducing pixel scale
Correct units??
correct

## Slide 14: Slope covariance
drop over larger distance on the same wfs
shift by the distance because 1&2 pointing on different direction
No correlation on independent axis
WFS1 x
WFS2 x
WFS1 y
WFS2 y
WFS1 x
WFS1 y
WFS2 x
WFS2 y
Need to reshape covariance to pupil shape for better analysis
nIters = 1000, loopTime=0.0025, scrnHeights=[20km],
windDirs = 90, r0=0.05, windSpeeds = 17.94m/s, L0=10m,
Tel=0.4m, subapFOV=16”, nxSubaps=8, pxlsPerSubap=16,
GSPosition = [0,1”] & [0,-1”]

## Slide 15: What am I doing again?
Usually slodar is in open loop
Solar mcao have data in close loop
Solar ao want to have slodar measurement along with it
Why solar ao wants slodar measurement?
  Profiling has more details in elevation
  Do literature research on this
That’s why it has to be pseudo open loop
Slodar in pseudo open loop
Pseudo-open loop = close loop slope + dm shape
In mcao

## Slide 16: Note
Im confident with soapy now
Now the slodar test run / study in open loop
  Check with people
Research why am I doing this/importance
Compare slodar in open loop vs pseudo open loop
  Pseudo open loop
Slodar without propagation  general cases
Slodar with propagation in atmosphere  open loop  Ryan
Slodar with propagation in atmosphere and dms  pseudo open loop